## Slide 1: CADD – FPGA Architecture
Vinay Reddy
Department of Electronics and Communication
Engineering

## Slide 2: Target Architectures

## Slide 3: DESIGN FLOW
Application behaviour
Algorithm
Programming Optimisation Architecture Fabrication Device

## Slide 4
TARGET ARCHITECTURES
Classification
Hard-wired
  Full-custom or Semi-custom
  Every new application, a new device
Programmable
  PLA, PALs, FPGA
  Functionality can be modified during deployment

## Slide 5: Programmable Architectures

## Slide 6
PROGRAMMABLE ARCHITECTURE
6
Programmable
  Customisable even after the device is ready
Programmability
  Compile time (One-time, Multiple times)
  Run-time

## Slide 7
PROGRAMMABLE LOGIC ARRAY
PLA
Sum-of-Products Array
  True and Complement
  Programmable AND + Programmable OR
Programmable switches
  Connect/disconnect
How?
  Fuse electrically

## Slide 8: PROGRAMMABLE ARRAY LOGIC
PAL
Sum-of-Products Array
  True and Complement
  Programmable AND + Fixed OR

## Slide 9
COMPLEX PLDs
CPLD
Evolutionary next step to PLAs
Higher densities
Complex logic functions
Interconnection wires

## Slide 10
FPGAs
Look-up table (LUT): Logic operations
Flip-Flop (FF): Stores the result of the LUT
Wires: Connect elements
Input/Output (I/O) pads: Data in and out of the FPGA.

## Slide 11: FPGA ARCHITECTURE
Programmable Logic
Programmable Routing

## Slide 12: LOGIC: LOOKUP TABLES
LUT
FF
LUT
FF
LUT
FF
LUT
FF
2K:1
MUX
2K
SRAM
K
Slice/Cluster

## Slide 13
LOOK-UP TABLE
2K SRAM Cells
22K different functions
2K:1 MUX
  K-levels of 2:1 muxes
2K:1
MUX
2K
SRAM
K

## Slide 14
LOOK-UP TABLE: 2-INPUTS
22 SRAM Cells
222 different functions
22:1 MUX
  2-levels of 2:1 muxes
22:1
MUX
22
SRAM
2

## Slide 15: LOGIC: SOFT
Programmable Logic
Blocks

## Slide 16: LOGIC: HARD BLOCKS
Memory
Blocks

## Slide 17: LOGIC: HARD BLOCKS
DSP
Blocks

## Slide 18: LOGIC: LOOKUP TABLES
LUT
FF
LUT
FF
LUT
FF
LUT
FF
2K:1
MUX
2K
SRAM
K
Slice/ Cluster

## Slide 19: OTHER TARGET ARCHITECTURES
Structured ASICs
  In-between ASICs and FPGAs
Processors
  Full-custom, but software programmable
System on Chips
  Processors, ASICs, Programmable logic, …,

## Slide 20: Basys 3 FPGA Board
The Basys 3 board is a complete, ready-to-use digital circuit development platform based on the latest Artix®-7 Field Programmable Gate Array (FPGA) from Xilinx®.

## Slide 21: OTHER TARGET ARCHITECTURES
The Xilinx (now AMD) part number
XC7A35T-1CPG236C breaks down into specific characteristics of a Field-Programmable Gate Array (FPGA).
Here is what each section means:
XC: Standard commercial Xilinx product.
7: 7 Series architecture, based on a 28-nanometer process technology.
A: Artix-7 family, which is optimized for low-power and high-throughput applications.
35T: Specific device within the Artix-7 family. The "35" indicates it has roughly 35,000 logic cells, and the "T" denotes that it includes transceivers.
-1: Speed grade, which is a performance indicator. For Xilinx, a smaller number typically means a lower speed and cost, while a higher number (e.g., -2 or -3) indicates higher performance.
CPG236: The package type and pin count. "CPG" specifies a 0.5 mm pitch Chip-Scale Ball Grid Array (CSBGA), and "236" refers to the number of solder balls (pins) on the package.
C: Temperature grade, indicating a commercial operating temperature range